## Slide 1: Modelling risk and evaluating mitigation measures
Russell Leaper

## Slide 2
Probability of a whale and vessel being in the same place at the same time
Probability of injury to the whale or damage to the vessel
Probability that no avoidance action taken by the whale or vessel
RISK
X
X
=
Routing measures
Long term e.g. TSS, ABTA
Short term - dynamic
Lookouts on vessels
Speed reduction
Acoustic alerts to whales
Speed reduction
Relative risk reduction due to mitigation measures
Possible mitigation measures

## Slide 3: Whale response to vessels
Most poorly understood and difficult to predict of all risk factors – no real quantitative data
Some risk models suggest whales must make some effective avoidance, otherwise mortality would be much higher than observed (Tregenza et al., 2005)
Can model acoustic propagation and noise from vessels to predict received levels for whales but difficult to predict response if any (e.g. Nowacek et al., 2004)
Reducing background noise levels noise by tackling the noisiest ships should help whales detect oncoming ships and reduce risk (Leaper et al., 2009)

## Slide 4: Vessel manoeuvres to avoid whales
Vessel manoeuvring capabilities generally well understood
Adequate data on sightings process from sightings surveys and dive times from behavioural studies
Can put an upper bound on the proportion of collisions that might be avoided by responding to a sighting for different types of vessel/speed/observer combinations (Clyne and Leaper, 2004)

## Slide 5: Simulation results for sightings of fin whales and avoidance by fast ferry (175m length)

## Slide 6: Probability of serious injury or vessel damage
Speed is dominant factor, less understanding of the implications of hull design
Analyses from available collision data (Vanderlaan and Taggart, 2007) suggest probabilty of lethal collision rises sharply with speed from 9 – 15 knots and approaches 1 for speeds >15knots
Hydrodynamic modelling (Knowlton et al., 1998; Silber et al., 2010) can be used to estimate impact force and consequences

## Slide 7: Predicting risk due to whales and ships in same place at same time
Most effective mitigation measure is to keep whales and ships apart
Need data on shipping density (AIS provides large data sets but limited by radio range. Satellite systems provide potentially comprehensive data)
Need data on whale density including variability in distribution patterns over time

## Slide 8
AIS data collected during whale surveys by IFAW, Alnitak and Tethys. Clear gaps in coverage. Red indicates location of a vessel travelling at >17 knots, yellow <17 knots. Level of shading highlights routes but cannot be used to estimate actual shipping density.

## Slide 9
Chart: Change in probability of receiving an AIS signal with distance from the receiver in different areas
| 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26 | 28 | 30 | 32 | 34 | 36 | 38 | 40 | 42 | 44 | 46 | 48 | 50 | 52 | 54 | 56 | 58 | 60 | 62 | 64 | 66 | 68 | 70 | 72 | 74 | 76 | 78 | 80
Eastern Mediterranean | 1 | 1 | 1 | 1 | 0.99923 | 0.99923 | 0.99769 | 0.99769 | 0.9946 | 0.99383 | 0.99228 | 0.98688 | 0.97994 | 0.97222 | 0.95756 | 0.94136 | 0.92207 | 0.90509 | 0.89583 | 0.8858 | 0.87269 | 0.86111 | 0.8588 | 0.85648 | 0.85108 | 0.84799 | 0.84568 | 0.84414 | 0.83873 | 0.83025 | 0.82022 | 0.81559 | 0.81096 | 0.80324 | 0.8017
Western Mediterranean | 1 | 0.98413 | 0.98413 | 0.98413 | 0.96825 | 0.95238 | 0.92063 | 0.90476 | 0.90476 | 0.88889 | 0.87302 | 0.87302 | 0.84127 | 0.80952 | 0.80952 | 0.80952 | 0.80952 | 0.80952 | 0.80952 | 0.79365 | 0.79365 | 0.79365 | 0.79365 | 0.77778 | 0.77778 | 0.7619 | 0.74603 | 0.73016 | 0.73016 | 0.71429 | 0.68254 | 0.66667 | 0.65079 | 0.65079 | 0.65079
NE Atlantic | 1 | 0.98571 | 0.96571 | 0.94 | 0.89143 | 0.84 | 0.76857 | 0.67714 | 0.60857 | 0.54 | 0.48571 | 0.42286 | 0.39143 | 0.36571 | 0.35429 | 0.34 | 0.33143 | 0.32571 | 0.31714 | 0.30286 | 0.29714 | 0.28286 | 0.27429 | 0.26571 | 0.25714 | 0.25714 | 0.25143 | 0.25143 | 0.24 | 0.23714 | 0.23714 | 0.23429 | 0.22857 | 0.22857 | 0.22286

## Slide 10
Alboran Sea surveys by Alnitak. Green track shows survey vessel with AIS receiver. Numbers show spot density measurements of shipping (km travelled per km2 per year)

## Slide 11
Observed shipping patterns following the change in the Cabo de Gata TSS and estimated densities of pilot whales from surveys by Alnitak.

## Slide 12
Ligurian Sea surveys by Tethys. Green track shows survey vessel with AIS receiver. Numbers show spot density measurements of shipping (km travelled per km2 per year)

## Slide 13
IFAW surveys in Eastern Mediterranean. AIS received locations Red dots >17knots.

## Slide 14
Green lines show track of research vessel Song of the Whale.
Black triangles show locations of acoustic detections of sperm whales.

## Slide 15
Spot density estimates of shipping (km travelled per km2 per year) plus speed profiles.

## Slide 16
A
B
Track from A to B 569.1nm. Including 15nm alteration to avoid observed whales, 570.2nm. 0.2% increase in distance.

## Slide 17: Route switching with visual observers as a possible mitigation measure for regular ferry transits

## Slide 18
Two route options a small distance apart through area of greatest likelihood of whales
Route on each crossing is chosen based on sightings on previous crossing
Potential to reduce risk through areas where whale distribution is difficult to predict but concentrations persist for a day or more
Comparisons of sightings rates allow risk reduction to be quantified

## Slide 19: Short term persistence of whale distribution patterns.
Data from 830 return ferry trips between Boston and Provincetown 2002-2009 collected by Whale Center of New England.

## Slide 20
Data from 830 return ferry trips between Boston and Provincetown 2002-2009 collected by Whale Center of New England.